## Slide 1: A Survey on Clustering Schemes
Jane Y. Yu and Peter H.J. Chong, “A Survey of Clustering Schemes For Mobile Ad Hoc Networks” IEEE Communications, Surveys, First quarter 2005, Vol. 7 No. 1.
Presented By Donghyun Kim September 5, 2008 Mobile Computing and Wireless Networking Research Group
at University of Texas at Dallas

## Slide 2: Introduction
MANETs (Mobile Ad-hoc Networks)
  Allow mobile terminals to set up a temporary network for instant communication without fixed infrastructures.
  A flat structure exclusively based on proactive or reactive routing schemes cannot perform well in a large dynamic MANET – Scalability Issue.
Presented by Donghyun Kim on September 5, 2008 Mobile Computing and Wireless Networking Research Group at The University of Texas at Dallas

## Slide 3: Introduction – cont’
Clustering?
  A clustering in networks is that the nodes in the network is partitioned into virtual groups by predefined rules.
  Nodes are divided into three groups - clusterhead, clustergateway, or clustermember
Presented by Donghyun Kim on September 5, 2008 Mobile Computing and Wireless Networking Research Group at The University of Texas at Dallas

## Slide 4: Introduction – cont’
Roles
  Clusterhead
    Normally serves as a local coordinator for its cluster, performing intra-cluster transmission arrangement, data forwarding, and so on.
  Clustergateway
    Non-clusterhead node with inter-cluster links, so it can access neighboring clusters and forward information between clusters.
  Clustermember - Else
Presented by Donghyun Kim on September 5, 2008 Mobile Computing and Wireless Networking Research Group at The University of Texas at Dallas

## Slide 5: Benefits of Clustering
A cluster structure, as an effective topology control means, there are at least three benefits.
  Facilitates the spatial reuse of resources to increase the system capacity, resulting in reducing collision, etc.
  Decrease routing overhead since less number of nodes will be involved in routing.
  Helps an ad hoc network more smaller and stable in the view of each mobile terminal.
Presented by Donghyun Kim on September 5, 2008 Mobile Computing and Wireless Networking Research Group at The University of Texas at Dallas

## Slide 6: Cost of Clustering
Constructing and maintaining a cluster structure usually requires additional cost compared with a flat-based MANET.
  In a dynamically changing scenario, clustering-related information exchange increases drastically.
  Ripple effect - some clustering schemes may cause the cluster structure to be completely rebuilt over the whole network when some local events take place.
  Frozen period - most schemes separate the clustering into two phases, cluster formation and maintenance, and assume mobile nodes keep static when cluster formation is in progress – may not applicable in real scenario.
  Timing issues - Since all nodes are not synchronized, cluster formation takes a long time.
Presented by Donghyun Kim on September 5, 2008 Mobile Computing and Wireless Networking Research Group at The University of Texas at Dallas

## Slide 7: Classification of Clustering Schemes
Clusterhead-based vs. Non-clusterhead-based
1-hop clustering vs. Multi-hops clustering
Based on objectives
  DS (Dominating Set)-based clustering
  Low-maintenance clustering
  Mobility-aware clustering
  Energy-efficient clustering
  Load-balancing clustering
  Combined-metrics-based clustering
Presented by Donghyun Kim on September 5, 2008 Mobile Computing and Wireless Networking Research Group at The University of Texas at Dallas

## Slide 8: DS-based Clustering
Goal
  Finding a connected dominating set to reduce the number of nodes participating in rout search or routing table maintenance.
Presented by Donghyun Kim on September 5, 2008 Mobile Computing and Wireless Networking Research Group at The University of Texas at Dallas

## Slide 9: Low-maintenance clustering
Goal
  Providing a cluster infrastructure for upper layer applications with minimized clustering-related maintenance cost (i.e. messages).
  Limiting re-affiliation and re-clustering events.
Summary
  LLC (Least Cluster Change)
    LIC (Lowest ID Clustering) - a node with highest ID becomes a cluster head.
    HCC (Highest Connectivity Clustering) - a node with highest local node degree becomes a cluster head.
    LCC – use LIC for the initial construction. When two clusters meet, one head retires. Nodes without an adjacent a head use LIC to build a new cluster.
  3hBAC (3-hop Between Adjacent Clusterheads)
    Forms a 1-hop non-overlapping cluster structure with three hops between neighboring clusterheads by introducing a new node status, named clusterguest (which is not adjacent to a head directly).
  Lin’s Algorithm
    An adaptive clustering scheme to form a non-overlapping cluster architecture without clusterheads because clusterheads bear extra work compared with ordinary member nodes and likely will become the bottlenecks of a network.
  PC (Passive Clustering)
    A node without an adjacent head piggybacks its claim with normal message.
    Each node is responsible for updating its own cluster status by keeping a timer.
Presented by Donghyun Kim on September 5, 2008 Mobile Computing and Wireless Networking Research Group at The University of Texas at Dallas

## Slide 10: Mobility-aware clustering
Goal
  Utilizing mobile nodes’ mobility behavior for cluster construction and maintenance and assigning mobile nodes with low relative speed to the same cluster to tighten the connection in such a cluster.
  By grouping mobile terminals with similar speed into the same cluster, the intra-cluster links can become more tightly connected.
Summary
  MOBIC
    Suggests that cluster formation, especially clusterhead election, should take mobility into consideration.
    Calculate the aggregate local speed and choose the one with the lowest mobility.
  DDCA (Distributed Dynamic Clustering Algorithm)
    Find a set of node such that a communication graph induced by them can be a complete graph with some probability for some duration.
Presented by Donghyun Kim on September 5, 2008 Mobile Computing and Wireless Networking Research Group at The University of Texas at Dallas

## Slide 11: Energy-efficient clustering
Goal
  Avoiding unnecessary energy consumption or balancing energy consumption for mobile nodes in order to prolong the lifetime of mobile terminals and a network.
Summary
  IDLBC (ID Load Balancing Clustering)
    A mobile node with the higher VID becomes a cluster head. VID is proportional to 1/(current energy level).
  Wu’s Algorithm
    DS-based Clustering
    A head retires if all of its members can be covered by other heads
  Ryu’s Algorithm
    Heads are pre-selected and can have a limited number of members.
    Assume transmission power is adjustable.
Presented by Donghyun Kim on September 5, 2008 Mobile Computing and Wireless Networking Research Group at The University of Texas at Dallas

## Slide 12: Load-balancing clustering
Goal
  Distributing the workload of a network more evenly into clusters by limiting the number of mobile nodes in each cluster in a defined range.
Summary
  AMC (Adaptive Multi-hop Clustering)
  BLBC (Degree-Load-Balancing Clustering)
    Initial cluster structure is given
    By exchanging messages, each cluster adjusts its size
    Differ in detail
Presented by Donghyun Kim on September 5, 2008 Mobile Computing and Wireless Networking Research Group at The University of Texas at Dallas

## Slide 13: Combined-metrics-based clustering
Goal
  Considering multiple metrics in cluster configuration, including node degree, mobility, battery energy, cluster size, etc., and adjusting their weighting factors for different application scenarios.
Summary
  On-Demand WCA (Weighted Clustering Algorithm)
    Followings are considered for electing a cluster head
      Degree-difference
      Sum of the distance with all neighbors
      Average moving speed
      Clusterhead serving time
Presented by Donghyun Kim on September 5, 2008 Mobile Computing and Wireless Networking Research Group at The University of Texas at Dallas