## Slide 1: Underwater Acoustic Sensor Networks: New Challenges
F. Akyildiz, D. Pompili, and T. Melodia, "Underwater acoustic sensor networks: Research challenges," Journal of Ad Hoc Network, vol. 3, no. 3, pp. 257-279, Mar. 2005.
Presented By Donghyun Kim September 12, 2008 Mobile Computing and Wireless Networking Research Group
at University of Texas at Dallas

## Slide 2: Underwater Sensor Networks?
Presented by Donghyun Kim on September 12, 2008 Mobile Computing and Wireless Networking Research Group at The University of Texas at Dallas
AMOUR (Autonomous Modular Optical Underwater Robot)
(Image Source: http://groups.csail.mit.edu/drl/wiki/images/d/db/amour_with_sensors.jpg)

## Slide 3: Motivation
Traditional approach for underwater monitoring
  Deploy underwater sensors that record data during the monitoring mission
  Recover the instruments
Drawbacks
  No real-time monitoring
  No on-line system reconfiguration
  No failure detection
  Limited storage capacity
Presented by Donghyun Kim on September 12, 2008 Mobile Computing and Wireless Networking Research Group at The University of Texas at Dallas

## Slide 4: Applications
Ocean sampling networks
Environmental monitoring
Undersea explorations
Disaster prevention
  Realtime constraint
Assisted navigation
Distributed tactical surveillance
  The location of sensors/observers have to be remained secure
Mine reconnaissance
Presented by Donghyun Kim on September 12, 2008 Mobile Computing and Wireless Networking Research Group at The University of Texas at Dallas

## Slide 5: History of Underwater Communication
During WWII (in 1945), an underwater telephone was developed to communicate with submarines.
Three types of wireless link
  Radio Frequency (RF) signal
    Only radio signal with extra low frequency (30-300Hz) can travel in sea water – Requires large antennae and high transmission power
  Optical link
    Optical waves are significantly affected by scattering
  Acoustic link
    Practical solution
Acoustic communications are the typical physical layer technology in underwater networks
Presented by Donghyun Kim on September 12, 2008 Mobile Computing and Wireless Networking Research Group at The University of Texas at Dallas

## Slide 6: Challenges
Bandwidth is severely limited
Underwater channel is severely impaired
  Due to multi-path and fading.
Long and variable Propagation delay
High bit error rates and temporary losses of connectivity
Battery power is limited
  Usually batteries cannot be recharged since solar energy cannot be exploited
Underwater sensors are prone to failures because of fouling and corrosion
Presented by Donghyun Kim on September 12, 2008 Mobile Computing and Wireless Networking Research Group at The University of Texas at Dallas

## Slide 7: Design Issues
Design Issue - underwater sensor networks are expensive
  Has to be highly reliable
  Have to avoid a failure by a single point
  No bottleneck
Three architectures
  Static two-dimensional UW-ASNs for ocean bottom monitoring
    Environmental monitoring
  Static three-dimensional UW-ASNs for ocean-column monitoring
    Surveillance application, monitoring of ocean phenomena
  Three-dimensional networks of autonomous underwater vehicles (AUVs).
Presented by Donghyun Kim on September 12, 2008 Mobile Computing and Wireless Networking Research Group at The University of Texas at Dallas

## Slide 8: Routing in USN
Multi-hop transmission is still efficient than direct transmission
Multi-hop routing incurs extra overheads
  For good routing decision, information has to be diffused and cause extra signaling and computation
Ideal routing scheme for USN
  exploiting multi-hop paths
  minimizing the signaling overhead necessary to construct underwater paths
Presented by Donghyun Kim on September 12, 2008 Mobile Computing and Wireless Networking Research Group at The University of Texas at Dallas

## Slide 9: Architecture for 2D underwater sensor networks
Presented by Donghyun Kim on September 12, 2008 Mobile Computing and Wireless Networking Research Group at The University of Texas at Dallas
(Image Source: http://www.ece.gatech.edu/research/labs/bwn/UWASN/figures/2D_arch.gif )

## Slide 10: Architecture for 3D underwater sensor networks.
Presented by Donghyun Kim on September 12, 2008 Mobile Computing and Wireless Networking Research Group at The University of Texas at Dallas
(Image Source: http://www.ece.gatech.edu/research/labs/bwn/UWASN/figures/3D_arch.gif )

## Slide 11: Sensor networks with Autonomous Underwater Vehicles (AUVs)
In experimental work, inexpensive AUV submarines equipped with multiple underwater sensors can reach any depth in the ocean
AUVs can be used for many purposes
  Requires new network coordination algorithms including
  Adaptive sampling (Where to AUVs should move?)
  Self-configuration (Has to be autonomous)
AUVs can recharge using solar cells
  Can survive several months
Presented by Donghyun Kim on September 12, 2008 Mobile Computing and Wireless Networking Research Group at The University of Texas at Dallas

## Slide 12: Basics of Acoustic Propagation
Underwater acoustic communications are mainly influenced by
  Path loss (by attenuation, geometric spreading)
  Noise (man made, ambient noise)
  Multi-path (some data is faster, strong function of depth and the distance between transmitter and receiver)
  Doppler spread (When receiver is moving, frequency and wavelength can be changed)
  High and variable propagation delay
Available bandwidth of the UnderWater Acoustic channel (UW-A) is limited and dramatically dependent on both range and frequency
Presented by Donghyun Kim on September 12, 2008 Mobile Computing and Wireless Networking Research Group at The University of Texas at Dallas

## Slide 13: Design Challenges
Differences with terrestrial sensor networks
  Cost – expensive (over $1000 vs. TSN $1)
  Deployment – (sparse vs. TSN dense)
  Communication Power – (higher)
  Memory – (caching might be possible)
  Spatial correlation (unlikely due to sparseness)
Presented by Donghyun Kim on September 12, 2008 Mobile Computing and Wireless Networking Research Group at The University of Texas at Dallas

## Slide 14: Design Challenges
Underwater Sensors
  The electronics are usually mounted on a frame which is protected by a PVC housing (Sometimes whole components are protected by frames)
  Challenges
    Nano-sensors
    Devise periodical cleaning mechanisms against corrosion and fouling
    Robust again temperature changes
    Synoptic sampling
Presented by Donghyun Kim on September 12, 2008 Mobile Computing and Wireless Networking Research Group at The University of Texas at Dallas

## Slide 15: A Cross-Layer Protocol Stack
Conventional layers
  Physical layer
  Data link layer
  Network layer
  Transport layer
  Application Layer
Application specific layers
  Power management plane
  Coordination plane
    Responsible for all functionalities that require coordination among sensors (i.e. sleep modes, data aggregation, etc.)
  Localization plane
Cross-layer design approach
  In the conventional layered approach, there has been lacks of information sharing across protocol layers, forcing the network to operate in a suboptimal mode.
  Need to use cross-layer design approach to use the scarce recourses better
  Modular design approach is preferred
Presented by Donghyun Kim on September 12, 2008 Mobile Computing and Wireless Networking Research Group at The University of Texas at Dallas

## Slide 16: USN Network Layer
The network layer is in charge of determining the path between a source and a destination node.
Taxonomy of routing protocols
  Proactive protocols (i.e. distance vector based)
    Minimize the message latency induced by route discovery
  Reactive protocols
    Discover a route if necessary (higher latency)
  Both of them incur excessive signaling overhead due to their extensive reliance on flooding
  Geographical routing protocols
    Utilize localization information
Presented by Donghyun Kim on September 12, 2008 Mobile Computing and Wireless Networking Research Group at The University of Texas at Dallas

## Slide 17: Research Issues for USN Network Layer
Need to develop algorithms to provide strict or loose latency bounds
Need to develop mechanisms (i.e. routing algorithm) to handle loss of connectivity without provoking immediate retransmissions
Algorithms and protocols need to detect and deal with disconnections due to failures, unforeseen mobility of nodes or battery depletion
Local route optimization algorithms are needed to react to consistent variations in the metrics describing the energy efficiency of the underwater channel
Localization algorithm
Presented by Donghyun Kim on September 12, 2008 Mobile Computing and Wireless Networking Research Group at The University of Texas at Dallas